# The basic functions of ADM -

# signal digitizing of medical TV-systems

- Entering necessary initial data on a patient and on medical personnel for subsequent import to graphic database.

- Choice of modes of shooting of patients: frame format, number of frames, pulse ratio (every n frame, 1<n<100).

- Real-time indication of preparation, start of acquisition, storage and data transmission modes of the ADM digitizer.

- Automatic dump of the series taken off to a Temporary Databank for subsequent viewing and import to a graphic database.

IMPORTANT! Requires AVGBase2000 database installed.

IMPORTANT! Requires MedDigiView viewing system installed.

### Software add-ons for ADM (subject to separate agreement):

- Target on-line view in a scopy mode with last frame displayed.

- Display of Roadmapping.

- Creation of cyclogram for equipment management.

- Creation of cyclogram to manage subtraction process.

## Specifications of ADM system DSP TMS320C6201 based

| TV-signal (ADM) digitizer w/o compression | 65 MHz/channel, 12b, S/N > 65dB, 50/60Hz. |
| --- | --- |
| Video data format H*V*2 (MB) (flexible, as defined by TV-system) | matrix from 576* 576*12b (16 bit/pixel) up to 1152*1152*12b (16 bit/pixel) |
| Optional extension for two-projection Angio systems | 1 ADM board (additional) |
| Optional extension of ADM for RGB configuration | up to 3 ADM (parallel) |
| Real time video processor | DSP, TMS320C6201 1600 MIPS / 1 board. |
| Global Video Memory GVM (PC RAM based) | min = 512MB, max = 4GB /1 board. |
| Number of frames in a series | from 1 to Nfrmax, where Nfrmax = (GVM – 128)/H*V*2 |
| Post-procedure server storage | HDD 720GB RAID 0/1/0+1 U160 SCSI |
| Optional storage extension | HDD 720GB RAID U160 SCSI / case |
| Long-term laser disk storage | 5.2GB DVD-RAM / disk. |
| Optional laser disk-drives | 1 - 6 DVD-RAM drive / case. |
| Universal intellectual interface | AS-UII-2k01 board |
| Network requirements | 1/2/4 channel 100Mbps Ethernet |
| PC requirements | PIII/800MHz, Intel BX/Gx/840/815EP |
| Graphic adapter requirements | 16/32MB Matrox G400, G450 SH/DH |
| Monitor requirements | ≥ 1600*1200*32b / 85fps |
| OS requirements | Windows NT 4.0 SP 6.0 |