## The basic functions of MedDigiView - system for viewing and image processing:

- Selection of graphic data for any patient from Temporary Databank with MedDigiView. Selection and loading of a series of shooting for viewing. Possibility for fast switch, if necessary, to viewing data of another patient, if such data already exists in Temporary Databank.

- Interactive viewing with loop, reverse and a step-by-step mode options, at a variation of scrolling speed in a cine-mode, choice of any range of frames in the series of shooting for scrolling.

- Digital filtration allows to apply up to 3 consecutive filters in real-time mode: image contouring, sharpness, bas-relief etc.

- LUT-manipulations with a choice of any of 6 functions - analogue of expanded brightness and contrast functions: square-law, logarithm, exponential and three trigonometry functions - (electronic level, window, nonlinear transformations, negative).

- A post-procedure real-time subtraction by the indicated range of mask and for group of subtracted frames. All variations of cine-mode and on step-by-step scrolling are available.

- Digital zoom, interactive viewing at chosen zoom scale. All variations of cine-mode and on step-by-step scrolling are available.

- Selection and exclusion of insignificant frames in series of shooting, after importing raw data to a graphic database from ADSP-50  digitizing system.

- Converter of chosen frame to *.TIFF format for individual operations with subsequent laser printout on paper or transparency film.

- Automatic recording of scenario for each set of manipulations when processing the series of the frames, optional subsequent saving and storage with possibility to run any existing scenarios.

- Creation of the significant frame for fast visualization in AGVBase-2k01database and in MedDigiView viewing and processing systems.

- Creation of comments to be added to the new series of frames received from ADSP-50  digitizing system.

### Program options (subject to separate agreement):

- Electronic shuttering of frame in series (rectangular, circular, any convex curve).

- Electronic selection of significant area of the frame in series for further processing and visualization within the limits of significant area only (rectangular, circular, any convex curve).

- Automatic histogram of the frame / series.

- Frame sequences summing in real time mode.

- Creating cyclograms with multi-mask subtraction.

- Creating the complex scenarios of data processing for series of shootings.

- Background laser printing.

- The converter of graphic and add-on data of patient’s shooting to DICOM3 file format.